## Slide 1: LADDER SAFETY
One Rung at a Time
Arkansas Workers’ Compensation Commission
Health & Safety Division

## Slide 2: Falls:
19% of Permanent
Disabilities
21% of Temporary Total
Disabilities

## Slide 3: Gravity
Never Forgets

## Slide 4: Ladder Safety Tips:
1. Inspect

## Slide 6: Ladder Safety Tips:
2. Resting on Stable, Solid Ground

## Slide 7: Ladder Safety Tips:
3. Don’t Climb too High for Your Ladder

## Slide 8: Ladder Safety Tips:
4. Keep Your Body Between the Side Rails

## Slide 9: Ladder Safety Tips:
5. Remember the “3-Point Rule”

## Slide 10: Ladder Safety Tips:
6. Face the Ladder When Going Up or Down

## Slide 11: Ladder Safety Tips:
7. One Person on a Ladder at a Time

## Slide 12: Ladder Safety Tips:
8. Use the Right Ladder For the Task

## Slide 13: Ladder Safety Tips:
9. Never Use Metal Ladders Around Electrical Wires or Equipment

## Slide 14: Ladder Safety Tips:
10. Ladders Should be as Compact as Possible

## Slide 15: Ladder Safety Tips:
11. Carry Ladders Properly

## Slide 16: Ladder Safety Tips:
12. Tie Ladders Off Before Using

## Slide 17: General Requirements for Ladders

## Slide 18: Types of Ladders
1. Portable
2. Step
3. Extension

## Slide 19: Portable Ladders
Inspection and Care
Check for:
1. Can it support 4 times the load
(3.3 times for extra heavy-duty type ladders)
2. Slip-resistant rungs or steps

## Slide 20: Step Ladders
Inspection and Care
Check for:
1. Make sure all 4 legs are in contact with the ground
2. Don’t use step ladders like straight ladders
3. Don’t use rear braces as steps
4. Make sure spreaders are locked

## Slide 21: Extension Ladders
Inspection and Care:
Check for:
1. Long enough for the job
* at least 3 feet above point of support
* can work without overreaching
2. Height adjusted only by user, and only when on ground
3. Base of ladder one quarter (1/4) working length of the ladder from the support wall

## Slide 22: Fixed Ladders
General Tips:
Check for:
1. Proper support of ladder and rungs
2. Proper length of ladder
3. Clearances between sides, front & back of ladder
4. Rungs designed to prevent slipping
5. Cages, wells, safety devices, self-retracting lifelines, platforms as required
6. Proper step-across distances, extensions of side rails above top level and flaring and clearance of rails

## Slide 23: Cages for fixed ladders
Inspection and Care
Check for:
1. Horizontal Bands:
* Fastened to rails or structure
* Spacing
2. Vertical Bars:
* Inside horizontal bands
* Fastened to horizontal bands
* Spacing

## Slide 24: Cages for fixed ladders (contd.)
Inspection and Care
Check for:
3. Size of cage
4. No projections inside cage
5. Bottom of cage flared
6. Top of cage 42-inches above platform

## Slide 25: Wells for Fixed Ladders
Inspection and Care
Check for:
1. Completely encircle ladder
2. Free of projections
3. Proper diameter and length

## Slide 26: Ladder Safety Devices and Support Systems
Inspection and Care
Must:
1. Withstand a 500 lb. drop test
2. Hands-free operation, going up or down
3. Activate 2 feet after a fall
4. Limit speed of descent to maximum of 7 feet per second
5. Length of lifeline
* 9 inches or less

## Slide 27: Mounting Fixed ladders
Inspection and Care
Check for:
1. Proper attachments
2. Mountings & installation - don’t reduce strength of the ladder
3. Side rails, steps & rungs for side-step ladders continuous in extension

## Slide 28
<footer>
<date/time>
That's all Folks!
Thank you!