## Slide 1: EYE SAFETY
Arkansas Workers’ Compensation Commission
Health and Safety Division

## Slide 2: ON-THE-JOB EYE INJURIES
1,000 occur each day
Costs $300 million each year
9 out of 10 could be avoided
Notes: Every day an estimated 1,000 eye injuries occur in American workplaces. The financial cost of these injuries is enormous - more than $300 million per year in lost production time, medical expenses, and workers’ compensation. No dollar figure can adequately reflect the personal toll these accidents take on the injured workers and their families.
Every year, approximately 100,000 workers suffer serious injuries. Of these, 9 out of 10 could have been avoided by following safety procedures and wearing appropriate eye protection.
Take a moment to think about possible eye hazards at your workplace. A 1980 survey by the Labor Department’s Bureau of Labor Statistics (BLS) of about 1,000 minor eye injuries reveals how and why many on-the-job accidents occur.

## Slide 3: EYE INJURIES
Why Me?!!
Notes: “Why me?”
What contributes to eye injuries at work?
>Not wearing eye protection.
BLS reports that nearly 3 out of every 5 workers injured were not wearing eye protection at the time of the accident.
>Wearing the wrong kind of eye protection for the job.
About 40 % of the injured workers were wearing some form of eye protection when the accident occurred. These workers were most likely wearing protective eyeglasses without side shields, though injuries among employees wearing full-cup of flat-fold side shields occurred as well.

## Slide 4: CAUSES OF EYE INJURIES
Physical
Chemical
Thermal/ Radiation
Notes: Most of the causes of eye injuries can be separated into 3 different categories:
1. Physical,
2. Chemical and
3. Thermal/Radiation

## Slide 5: ON-THE-JOB EYE HAZARDS
High-Speed Particles
Notes: Physical:
Flying Particles - BLS found that almost 70% of the accidents studied resulted from flying or falling objects or sparks striking the eye. Injured workers estimated that nearly 60% of the objects were smaller than a pin head. Most of the particles were said to be traveling faster than a hand-thrown object when the accident occurred.

## Slide 6: ON-THE-JOB HAZARDS
Contact With Objects
Notes: Contact with objects: Pipes and blunt tools
Sharp or pointed tools: Nail guns, awls and screwdrivers, etc.

## Slide 7: ON-THE-JOB EYE HAZARDS
Chemicals, Fumes & Heat
Arkansas
Arkansas
Notes: Chemicals, Fumes and Heat
Contact with chemicals caused 20% of the injuries.
Other accidents were caused by objects swinging from fixed or attached positions, like tree limbs, ropes, chains, or tools which were pulled into eye while the worker was using them.

## Slide 8: ON-THE-JOB EYE HAZARDS
Welding/ Laser Hazards
Notes: Thermal/Radiation
Welding hazards: Ultraviolet light and sparks
Laser hazards: Exposed to non-ionizing radiation

## Slide 9: WHO GETS EYE INJURIES?
Craft Workers - 40%
Machine Operators - 30%
Construction - 20%
Notes: Where Do Accidents Occur Most Often?
Craft work in industrial equipment operations.
BLS reports 40% of injuries occurred among craft workers, i.e. mechanics, repairers, carpenters and plumbers. Almost half of the injured workers were employed in manufacturing, and only a little more than 20% were in construction.

## Slide 10: PREVENTING EYE INJURIES
Engineering Controls
Choosing & Wearing Protective Eyewear
Proper Training
Equipment Maintenance
Notes: How Can Eye Injuries Be Prevented?
To be effective, eye protection must be the appropriate type for the hazard encountered and properly fitted. 94% of the eye injuries to workers who were wearing eye protection resulted because of improper fit.
Prevention of eye injuries is five-fold:
1. Hazard Assessment of the workplace,
2. Eliminate the potential hazards by changing work practices and/or implementing engineering controls,
3. Selection of protective eyewear appropriate for the specific hazards,
4. Proper training in the use of eye protection, and
5. Proper maintenance of the equipment.
What is a “Hazard Assessment”?
A Hazard Assessment of the workplace must be conducted to determine if eye protection should be worn when employees are performing certain tasks and what is the appropriate eye protection for the specific hazard(s) that might be encountered. Eye protection must be provided for employees whenever there is a potential for eye injuries during the performance of their job, if work practices or engineering controls do not eliminate the risk of injury. Some things that should be considered to cause eye injuries include:
>Dust and other flying particles, such as wood dust, metal shavings or fibers.
>Molten metal that could splash in the eyes.
>Acids or caustic chemicals that could splash.
>Blood or other potentially infectious body fluids that could splash or splatter.
>Intense light that might be created by welding arcs or lasers.

## Slide 11: PREVENTING EYE INJURIES
Engineering Controls
Notes: Eliminate the Potential Hazards by Changing Work Practices or Implementing Engineering Controls
>Changing Work Practices
Example: When conducting the Hazard Assessment, if you discover that employees in the wood shop are cleaning off counter tops, equipment and the floor by using compressed air, the potential for eye injuries from flying particles during that particular task can be eliminated by changing the work practice from the use of compressed air to vacuuming the work area.
>Implement Engineering Controls
Example: If employees are physically dipping parts in an acid bath, there is a potential for eye injuries from the splashing of the acid. If the parts could be dipped in the acid bath by mechanical means instead, the potential hazard (splashing acid) for eye injuries will be eliminated with an engineering control.

## Slide 12: PREVENTING EYE INJURIES
Choosing & Wearing Protective Eyewear
40% of Injured Employees Were Wearing the Wrong PPE When They Got Hurt
Notes: Selection of the Appropriate Eye Protection
If the potential hazards cannot be eliminated by changing work practices or implementing engineering controls, protective eyewear must be worn by employees.
Each kind of protective eyewear is designed to protect against specific hazards. The OSHA Publication 3151, Assessing the Need for Personal Protective Equipment: A Guide For Small Business Employers (can be retrieved off OSHA’s Web page, www.osha.gov) Provides tables that can help you select the protective eyewear for your employees that is most appropriate to protect them from the specific hazards in your workplace.
Welding and laser operations require lenses to be tinted sufficiently to protect against the specific intensity of light created during the performance of the tasks.
Eyeglasses with prescription lenses designed for ordinary wear do not provide the level of protection necessary to protect against workplace hazards. Employees who wear eyeglasses with corrective lenses can be protected from eye injuries by wearing eye protection such as the following:
>Prescription safety glasses, with sideshields and protective lenses that meet the requirements of ANSI Z87.1.
>Goggles that fit comfortable over the corrective eyeglasses without disturbing the ailment of the eyeglasses.
>Goggles that incorporate corrective lenses mounted behind protective lenses.

## Slide 13: PREVENTING EYE INJURIES
Proper Training
What to Wear
When to Wear It
Notes: Training and Education
BLS reported that most workers were hurt while doing their regular jobs. Most injured workers said they believed eye protection wasn’t required by the situation. When asked, 40% of workers said they received no information on where and what kind of eyewear was available.
Each employee who is required to wear protective eyewear must be trained to know:
>When protective eyewear is necessary,
>What protective eyewear is necessary,
>How to wear the protective eyewear properly,
>The limitations of the protective eyewear, and
>The proper care, maintenance, useful life and disposal of the protective eyewear.

## Slide 14: PREVENTING EYE INJURIES
Maintenance of PPE
Proper Fit
Clean as Needed
Proper Storage
Notes: Maintenance
Eye protection devices must be properly maintained. Proper maintenance should include the following:
>Adjust eyewear to make sure it fits snugly and is reasonably comfortable.
>Secure any loose parts and replace lenses if they are scratched, cracked, pitted, faded, etc.
>Clean the eyewear after each shift or as needed according to the manufacturer’s instructions. Disinfect eyewear that is shared by several workers. Wash glasses with soap and water and rinse thoroughly. Then use a disinfectant and hang up to dry in a clean place.
>Store the eyewear in a case to prevent scratching and ensure continued good vision. To reduce or eliminate fogging, use special anti-fogging products.
>Label eyewear with the name of the assigned person. Each employee should be held responsible for inspecting his/her own safety glasses.

## Slide 15: PROTECTIVE EYEWEAR
Safety Glasses with Sideshields
Safety Goggles
Face Shields
Chemical Goggles
Notes: Protective Eyewear
>Types of Safety Eyewear:
Safety Glasses
Safety Goggles
Face Shields
Chemical Goggles
>Types of Lenses:
Glass
Plastic
Phototropic

## Slide 16: FIRST AID FOR EYE INJURIES
Burns
Flush with Water for 15 minutes
Get Medical Attention Immediately
Do Not Bandage or Use an Eye Cup
Notes: First Aid for Eye Injuries:
Burns From Chemical Splashes:
Flush the eye with water, with the eyelid pulled open, for 15 minutes or longer. Never use an eye cup or bandage to cover the eye. Consult a physician immediately. (Take the MSDS of the offending chemical with you to the doctor’s office.)

## Slide 17: FIRST AID FOR EYE INJURIES
Specks in the Eye
Lift Upper Eyelid Outward and Down Over Lower Lid
Let Tears Flush Specks
Keep Eye Closed & Bandaged Lightly
If Speck Doesn’t Wash Out – See a Doctor
Don’t Rub Eyes
Notes: Specks, Dust and Debris
    Pull the eyelid out and down, and let the natural tears wash the particle out. Do Not Rub the Eye. Consult a physician immediately.

## Slide 18: FIRST AID FOR EYE INJURIES
Cuts & Punctures
Bandage Lightly
See a Doctor
Do Not Wash the Eye
Do Not Try to Remove Objects Stuck in the Eye
Notes: Cuts and Punctures
    Lightly bandage cuts and punctures. Never flush or remove object stuck in the eye. Consult a physician immediately.

## Slide 19: FIRST AID FOR EYE INJURIES
Blows
Apply Cold Compresses
See a Doctor If Discoloration of Skin Occurs
Notes: Blows to the Eye
Apply a cold compress for 15 minutes. Consult a physician immediately.

## Slide 20: EYES One Pair Per Customer
Protect the Ones
You Have
Notes: Protect Your Eyes - They’re the Only Pair You Have!

## Slide 21
THANK YOU!