## Slide 1
LOCKOUT/TAGOUT
Arkansas Workers’ Compensation Commission
Health & Safety Division

## Slide 2: What is “Lockout/Tagout”?
It ensures that all potential energy sources are disconnected from equipment before maintenance, repair, cleaning or any other action that could get you hurt if the machine is accidentally turned on.

## Slide 3: Potential Energy Sources?
Any type of energy that is stored and can be accidentally released.
Gravity:
Like a rock on top of a hill – not a problem ‘til someone starts rolling it downhill.

## Slide 4: Potential Energy Sources Found in the Workplace
Electrical: Generated or Static
Mechanical: Like a coiled spring ready to release
Thermal: Steam or heated systems
Chemical Energy: Released during chemical reactions
Hydraulic, vacuum or pneumatic pressure

## Slide 5
Identify all potential energy sources

## Slide 6
Have complete written Energy Control Procedures to explain how to de-energize each piece of equipment
Energy Control Procedures
1.
2.
3.
4.

## Slide 7: Lockout Procedures
Lockout is used to prevent the release of hazardous energy, or to prevent the hazardous energy from escaping.
A padlock is placed on the appropriate energy isolating device that is in the off, or closed, position.

## Slide 8: Tagout Procedures
Put the tag on the equipment noting that it should not be used.
Put the date and your name
This is not the best way to ensure the equipment cannot be turned on accidentally, because tags can be removed or ignored.

## Slide 9: The “Fatal Five” Main Causes of Lockout/Tagout Injuries
Failure to stop equipment
Failure to disconnect from power source
Failure to dissipate (bleed, neutralize) residual energy
Accidental re-starting of equipment
Failure to clear work areas before restarting

## Slide 10: Who Performs Lockout/Tagout?
One who locks out equipment in order to perform the servicing or maintenance on that equipment.
Authorized Employee

## Slide 11: Affected Employee
One whose job requires him/her to operate equipment on which servicing or maintenance is being performed under lockout, or whose job requires him/her to work in an area in which such servicing or maintenance is being performed.

## Slide 12: What are.....?
prevent the transmission or release of energy.
Energy Isolating Devices
Mechanical devices that physically

## Slide 13: What are.....?
Written Energy Control Procedure
Written step-by-step procedures detailing how each piece of equipment is completely de-energized.
This also includes provisions for inspecting the procedures and training employees in the lockout/tagout procedures.
Energy Control Procedures

## Slide 14: Types of Lockout Devices
Plug Locks
Ball Valve Lockout
Gate Valve Lockout
Group Lockout Hasp
Electrical
Hydraulic, pneumatic, and other pressurized systems

## Slide 15: Basic Steps for Lockout/Tagout
Identify all potential energy sources.
Determine how the sources can be safely locked out.
Get all the locks you will need.
Alert the operator(s) that power is being disconnected.

## Slide 16
Make sure there is only one (1) key for each lock.
Note:

## Slide 17
Train everyone who will be involved in lockout/tagout of equipment, such as the supervisors, maintenance, production, etc.
Lockout/Tagout Procedures

## Slide 18
Prepare for shutdown.
Turn off equipment.
Isolate all energy sources: block moveable parts, drain or bleed hydraulic lines, disconnect electricity, etc.

## Slide 19
Apply lockout devices.
Control/or release any stored energy.
Verify that the equipment is completely de-energized. Make sure everyone is safely out of the way; then try starting the machine to make sure it is completely shutdown.

## Slide 20: Removal of Lockout and Restarting Equipment
Ensure equipment is safe to operate.
Safeguard all employees.
Remove lockout/tagout devices. Except in emergencies, each device must be removed by the person who put it on.
Last person to take off lock notifies affected employees of the status of the equipment.
Follow checklist to re-energize equipment.

## Slide 21: Temporarily Reactivating Equipment
Remove unnecessary tools from the work area and make sure everyone is clear of the equipment.
Remove lockout/tagout devices and re-energize the system.
As soon as the energy is no longer needed, isolate the equipment and re-apply lockout/tagout.

## Slide 22: Special Situations
Servicing lasts longer than one shift.
Contractors are performing service or maintenance at your workplace.
Worker who applied lock is not available.

## Slide 23: Tidbits of Information
Never attempt lockout/tagout procedures unless you have been trained and certified by your employer under an approved Energy Control Program.
Never loan or share your lock, combination, or key with anybody else.

## Slide 24
Always be sure all lockout/tagout devices are compatible with the environment in which they will be used, i.e. corrosive, humid, etc.

## Slide 25
Any Questions?

## Slide 26
Thank You!