## Slide 1
ELECTRICAL SAFETY
Arkansas Workers’ Compensation Commission
Health & Safety Division

## Slide 2: Introduction
Electricity is an essential part of modern life . Without it, we wouldn’t have lights, refrigeration, computers, TV’s, stereos, etc., etc., etc.

## Slide 3: Remember -Electricity can also be very DANGEROUS!
Every year, more than 1,000 employees are killed, and
Another 30,000 are injured from electrical shock.
Most of the injuries could have been prevented.

## Slide 4
Did you know that just 100 mA flowing through the body for only 2 seconds can cause death?
Why, a portable drill draws about 30 times that amount of current!

## Slide 5
The “Let Go” threshold that prevents you from releasing your grip of an exposed electrical wire is about 10-20 mA.

## Slide 6: OSHA Regulations
29 CFR 1910, Subpart S - Electrical Standards
29 CFR 1910.147 - Lockout/Tagout
29 CFR 1910.137 - Personal Protective Equipment

## Slide 7: What is Electricity?
“The physical phenomena arising from the behavior of electrons and protons that is caused by the attraction of particles with opposite charges and the repulsion of particles with the same charge.”

## Slide 8: Huh?
Let’s explain that differently.....

## Slide 9
A reservoir
A pipe
A source of pressure
Think of electricity like water flowing through a pipe.
For the water to flow, you must have:

## Slide 10
The reservoir: the source of electricity could be a battery, a generator or a power station.
The pipe: any conductor of electricity, like a wire, air, water... even a human body.
The source of pressure: the voltage drives the charged electrons.

## Slide 11
What is “Current”? Just like in a stream, current is the flow of electric charge.
What about “Voltage”? Voltage is the pressure, or the push, that drives the electricity forward.
How about “Resistance”? -Think of the resistance as the friction between the walls of a pipe and the water. Any electrical appliance is a resistor.

## Slide 12: OHM’S Law
I = E/R
I = Intensity, or Current (amps)
E = Electromotive force, or Voltage
R = Resistance, or Ohms

## Slide 13: Electrical Hazards
Shock
Burns
Arc-Blast
Explosions
Fires

## Slide 14: Shocks
Direct -
Currents of 30 mA or more can cause death.
Indirect -
Human reactions can result in falls or sudden movement into machinery.

## Slide 15: A shock can occur when there is:
Contact with both wires of an electrical circuit
Contact with a wire and the ground source
Contact with a ground source and a metal part that is in contact with the circuit

## Slide 16: Burns
Results when “hot” wires or equipment is touched. Typically, it’s the hands that are burned.

## Slide 17: Arc- Blast
Thermal Radiation
Pressure Wave
Projectiles

## Slide 18: Explosions
Occur when electricity provides a source of ignition in a potentially explosive atmosphere.

## Slide 19: Fires
Electricity is one of the most common causes of fire in homes and workplaces.

## Slide 20: The effects of shock depend upon:
Current and voltage
Resistance
Path through the body
Duration of shock

## Slide 21: Current and Voltage
Although high voltages can produce massive destruction of tissue upon contact, the most harmful effects of electrical shock are due to the current.

## Slide 22
Currents greater than 10 mA can produce painful to severe shock.
Currents between 100 to 200 mA can be lethal.

## Slide 23: Resistance
        Resistance of the human body varies with the amount of moisture on the skin. The drier the skin, the higher the resistance.

## Slide 24: Path through the body:
When current flows from hand to feet, the path includes both the heart and the lungs.
This type of shock can be fatal!

## Slide 25: Duration of shock:
If the shock is of short duration, it may only be painful.
But, a current of 100 mA flowing through your body for just a few seconds can be fatal.

## Slide 26: Minimize the Hazards
Lockout/Tagout
Guarding
Grounding
Mechanical Devices
Assured Equipment Grounding Program

## Slide 27: Minimize the Hazards (contd.)
Personal Protective Equipment
Safe Work Practices
Working at Heights

## Slide 28: Lockout/Tagout
Lock out energy in the off position.
Attach tags prohibiting their removal.
Take some additional safety measures if a lock cannot attached.

## Slide 29
Verify absence of power.
Discharge any stored energy.
Locks and tags can only be removed by the person who locked/tagged out the equipment, or by a supervisor.

## Slide 30: Guarding
Electrical equipment of 50 volts or more must be guarded by:Location in a locked room
Screens or partitions
Elevation of 8 feet or more above the floor or platform
Entrances to locations with live parts must be marked with warning signs.

## Slide 31: Grounding
All metal parts of equipment must be grounded if the equipment is:
  Near any other grounded equipment
  Located in a wet location
  Connected by a cord or a plug

## Slide 32: Mechanical Protection Devices
Fuses and circuit breakers protect equipment and wiring.
Fuses melt when too much current flows through them.
Circuit breakers trip open the circuit.

## Slide 33
An aisle at least 3 feet wide must be maintained in front of circuit breaker panels.
Circuit breaker panel covers should remain closed.
Circuit breaker panels should have a directory index.

## Slide 34
There should be no missing breakers or any other open spaces in breaker panels.
Never secure a breaker in the “closed”, or ON position.
Never tape a breaker in the “open” or OFF position.

## Slide 35: Ground Fault Circuit Interrupter GFCI
GFCIs protect people.
GFCIs will shut off electrical power within 1/40th of a second when it detects a difference of 5 mA or more.
GFCIs must be used when tools and extension cords are used on construction sites and near water.

## Slide 36: Assured Equipment Grounding Program
A scheduled system for testing electrical tools and extension cords.
Written description of specific procedures.
Helps assure that risks of electrical hazards are prevented/eliminated.
Competent person must be designated.

## Slide 37
Rubber gloves
Class B hard hats
Safety glasses
Face shields
Insulated boots
Insulated arm mats or sleeving
Take off all jewelry, rings and metal wristwatches.

## Slide 38: Portable Equipment
Hand tools:
Must have insulated grips
Should not have cracks, tears or gaps in the insulation

## Slide 39
Power tools:
Must be double-insulated or third-wire cord grounded, or GFCI installed.
Inspect tools for wear or defects.
Check safety guards or shields.
Inspect power cords and switches for cuts, frayed insulation and loose connections.

## Slide 40
Meters and Test Equipment:
Choose test equipment right for the job.
Never exceed limitations of test equipment.
Inspect meters and testers for safe operation.
Check probes and probe leads for defects.
De-energize circuit before re-connecting.

## Slide 41: Electrical Plugs and Extension Cords
Make sure extension cords are the right size for the tools being used.
Always use grounded electrical outlets and don’t overload.
Never remove the grounding post from a 3-prong plug.
Use a standard plug adapter and attach the ground properly.

## Slide 42: Electrical Cords
Inspect cords regularly for wear or cracks in insulation.
Keep cords and cables clean and free from kinks.
Never carry a tool by its cord.
Never cut off the grounding plug from a cord!

## Slide 43: Working at Heights
Always use non-conductive wooden or fiberglass ladders.
Never use aluminum ladders.
Use rubber caps to give protection from shocks and skids.
Stay at least 10 feet away when voltages are 50 kV or less; further away if voltages are greater.

## Slide 44: Safe Work Practices
Never work around electricity when you, your tools or clothes are wet.
Don’t work on electricity in the rain.
Make sure there are no atmospheric hazards such as dust particles, flammable vapors or excess oxygen.
Always work with adequate lighting.

## Slide 45
Don’t assume hazard is low when voltage is low.
Bond and ground all work benches.
Wear lineman’s rubber gloves on both hands.
Never lean on a metal rail or stand in a puddle of water.
Never work alone on a live circuit. Always have a partner who is CPR trained.

## Slide 46
Thank You!