## Slide 1
Arkansas Workers’ Compensation Commission
Health and Safety Division
Machine Guarding

## Slide 2
Machine guarding must be provided and maintained:
To protect machine operators and others
From hazards associated with operation of machines

## Slide 3
Hazards include:
In-going nip points
Rotating parts
Flying chips and sparks

## Slide 4
Rotating:
In-running nip points, spindles, shaft ends, couplings

## Slide 5
Reciprocating:
Back-and-forth, up-and-down
Reciprocating saw

## Slide 6
Transverse:
Movement in a straight, continuous line
Table saw

## Slide 7
Cutting:
Bandsaws, drills, milling machines, lathes
Bandsaw
Lathe
Milling machine

## Slide 8
Punching:
Punch presses, notchers
Punch press
Notcher

## Slide 9
Shearing:
Mechanical, pneumatic, or hydraulic shears
Hydraulic Shear

## Slide 10
Bending:
Press brakes, tube benders, plate rolls
Press brake

## Slide 11
Machine guards must be installed and maintained to:
Prevent contact
Remain secure
Protect from falling objects

## Slide 12
Machine guards must be installed and maintained to:
Create no new hazards
Create no interference

## Slide 13
Allow Safe Maintenance and Lubrication
You should be able to lubricate the machine without removing the safeguard.

## Slide 14
Barriers and guards
  Prevents contact
Mechanical or electronic devices
  Restricts contact, e.g. presence-sensing, restraining, tripping devices, 2-hand controls
Feeding and ejection methods
  Eliminates parts handling
Aids
  Warning signs
Types of Machine Safeguards:

## Slide 15
Training:
Identification of hazards
Description of safeguards
Instructions on how to use safeguards.
Instructions on how and when safeguards may be removed
Instructions on what to do if safeguard is missing, damaged, or inadequate

## Slide 16
GRINDER SAFETY

## Slide 17
Always protect your eyes when using a bench or floor grinder – wear only an eye or face shield bearing the logo ANSI Z-87.
Make sure the manufacturer’s recommended speed, as posted on the wheel, is compatible with your grinder.

## Slide 18
Be sure the outer wheel guard is in place
Be sure the power transmission cover is securely in place
Maintain the tool rest within 1/8” of grinding wheel*
Mount the grinder securely
Maintain the tongue guard within ¼” of grinding wheel*

## Slide 19
*As the wheel wears down, readjust the tool rest and tongue guard. When you can no longer adjust them, replace the wheel.
Important: When installing a new wheel, follow the manufacturer’s instructions closely. An improperly installed wheel can break and cause injury.

## Slide 20
Thank you!