## Slide 1: Hazard Communication Training
Arkansas Workers’ Compensation Commission
Health and Safety Division

## Slide 2
Purpose of the standard
Development of the standard
The 4 components of the standard:
  Written Program
  Chemical Inventory and Material Safety Data Sheets (MSDSs)
  Labels
  Training
Exposure Routes
Exposure Controls
Types of Exposures

## Slide 3: This standard was written to ensure that people who work with hazardous chemicals have the information they need to work with them safely.

## Slide 4: The Hazard Communication (HazCom) Standard, also known as the “Right to Know” Standard, was developed by the Occupational Safety and Health Administration (OSHA).
OSHA

## Slide 5: There are 4 components to the Hazard Communication Standard:
Written Hazard Communication Program
Chemical Inventory and Material Safety Data Sheets (MSDSs)
Labeling
Training

## Slide 6: 1. Written Hazard Communication Program
The written program should describe how the other requirements of the standard will be implemented and maintained.

## Slide 7: 2. Chemical Inventory and Material Safety Data Sheets (MSDSs)
Maintaining an up-to-date chemical inventory and the corresponding Material Safety Data Sheets (MSDSs) for all hazardous chemicals.

## Slide 8: What is a MSDS?
A Material Safety Data Sheet, or MSDS, is an information sheet which tells you all you need to know to work with a chemical safely.
MSDS

## Slide 9: What information does an MSDS give you?
Name of Chemical
Manufacturer
Chemical Components
Hazards Associated with the Product
Physical/ Chemical Characteristics

## Slide 10: And there’s more! They also provide you with:
Reactivity Data
Safe Handling & Use
Control Measures (PPE)
Spill and Leak Handling
First Aid/Emergency Response
Disposal Practices
MSDS

## Slide 11
Employers must ensure that MSDSs and inventories are immediately available to employees, and that they are updated when necessary.
Safety Guy

## Slide 12: At most companies, MSDSs can be found in the following locations:
Within each department
In the Safety Office
MSDS

## Slide 13: Who supplies MSDSs to product users?
All manufacturers of hazardous chemicals are required to provide one of these sheets for all products they sell.

## Slide 14: 3. Labeling
Labeling of all hazardous chemicals in the proper manner

## Slide 15: All labels must contain the following information:
Name of the product
Hazards associated with the product
Name and address of the manufacturer

## Slide 16
When you transfer a chemical to a smaller, or different container, you must label the new container.
There are 2 labeling systems.
  One of them is the National Fire Protection Association’s (NFPA's) labeling system.
Do you know what this label means?

## Slide 18
The other labeling system is the Hazardous Materials Information System (HMIS).
The HMIS system operates on the same principle as the NFPA diamond.

## Slide 19: Key To HMIS Label Numerical Ratings

## Slide 20: Training
Workers must be trained on hazards associated with the chemicals which they use, and how to use these products safely.

## Slide 21: Did you know that no matter where you work, you could be exposed to hazardous chemicals? You may not have anything hazardous, but your neighbor may!

## Slide 22: There are 4 ways that chemicals can get into your body.
Do you know what they are?

## Slide 23: 1. Inhalation
You can inhale chemicals in the form of fumes, vapors, gasses, or aerosols.

## Slide 24: 2. Ingestion
You can ingest chemicals directly through accidental intake, or indirectly through intake of contaminated materials.

## Slide 25: 3. Skin Absorption
Chemicals can also go directly through the skin. This is known as a dermal exposure, or skin absorption.

## Slide 26: 4. Injection
Finally, you can also be injected with a chemical agent via a needle stick, or by being punctured with any other type of “sharp” which has been contaminated.

## Slide 27
It is possible to work safely with hazardous chemicals as long as you know how to prevent unnecessary or excessive exposures.
How can you protect yourself from a chemical exposure?

## Slide 28: Engineering Controls
The preferred way to reduce or eliminate exposures, or potential exposures, is to “Engineer” the problem out. A good example of this type of control measure would be a chemical fume hood or the redesign of a ventilation system.

## Slide 29
An Engineering Control is one which modifies the source or reduces the amount of contaminant released into the work environment.

## Slide 30: Administrative Controls
The second preference, are methods of controlling employee exposure by job rotation, work assignment, time periods away from the hazard, or training in specific work practices designed to reduce the exposure.

## Slide 31: Personal Protective Equipment
This method of controlling hazards is always the last resort since it relies on people to protect themselves.

## Slide 32
When it is not economically or technically feasible to design and implement engineering controls, and administrative controls are not an option, employees must be provided personal protective equipment (PPE).

## Slide 33
This equipment must protect them from the specific hazards associated with the chemicals with which they work.

## Slide 34: Chemical exposures can be classified into 2 categories:
Acute
Chronic
2002
2003
2004
2005
2006

## Slide 35
An acute exposure is one which is a single, brief exposure, and the effects are immediate.
Effects can range from mild irritation to death.
Generally speaking, if it doesn’t kill you, you’ll recover completely.

## Slide 36
A chronic exposure is persistent, prolonged, and repeated.
If you are exposed in this manner, usually, by the time you recognize the symptoms of an adverse effect, it is too late. You already have some type of permanent systemic damage.

## Slide 37
Now it's time to find out how much you've learned. It’s QUIZ Time!

## Slide 38: 1. What are the 4 components of the Hazard Communication Program?
Engineering, administrative controls, ventilation and personal protective equipment
Health, fire, reactivity and special information
Inhalation, ingestion, absorption, and injection information
Written program, labels, MSDSs, and training


## Slide 39: 2. Which color on the NFPA label provides flammability hazard information?
Blue
Red
Yellow
White


## Slide 40: 3. If a chemical gives off vapors, what is the most likely route of exposure?
Dermal
Inhalation
Ingestion
Injection


## Slide 41: 4. MSDS is an abbreviation for which of the following.
Management of Safe Devices and Systems
Maintenance and Storage of Demons and Snakes
Material Safety Data Sheets
Management, Storage and Distribution of Substances


## Slide 42: 5. Which color on the NFPA label provides reactivity hazard information?
Red
Blue
White
Yellow


## Slide 43: 6. Which color on the NFPA label provides health hazard information?
Blue
Red
Yellow
White


## Slide 44: 7. Other than in the work area, where can MSDSs be obtained?
Safety Office and the manufacturer
Internet web pages
MSDSs are only available in the work area
Only from the Safety Office


## Slide 45: 8. Which of the following is an example of an engineering control?
Laboratory fume hoods
Limiting quantity of chemical used
Protective gloves
Respirators


## Slide 46: 9. Which three pieces of information are required to be on the product label?
Health, fire, and reactivity information
Identity of the hazardous chemical(s), appropriate warning and name/address of the manufacturer
Inhalation, ingestion, and absorption
Labels, MSDSs, and training


## Slide 47: 10. What are the four routes of entry?
Health, Fire, Reactive and Radioactive
Internal, External, Distal and Median
Ingestion, Inhalation, Injection and Abdominal
Ingestion, Inhalation, Skin Absorption and Injection


## Slide 48
THANK YOU!